_____________________________________________________

Product Information Version-1.0

www.qanon-audio.com

_____________________________________________________

Product Information Version-1.0

Features

- 12inch Full range coaxial monitoring

- Maximum SPL 124dB

- 1 x 12 "ferrite low frequency drive unit"

- 1 x 1.75 "ferrite high frequency drive unit"

- 90 degree horizontal coverage angle

- 60 degree vertical coverage angle

- Monitoring angle (1) 55 degrees

- Monitoring angle (2) 20 degrees

- Ground stacking integrated assembly system

- Install ⌀35mm pole socket

- 13x M8 threaded insert

TC12

QANON AUDIO TC12 is 2-way full frequency coaxial structure and high performance stage monitor, provide the frequency range of 60Hz-18kHz，Composed of a 12 inch low frequency and 1.75 inch high frequency compression unit, the constant directional diffusion angle, with a custom unit and waveguide technology,90 degree x 60 degrees can accurately cover the stage area . The monitor is matched with two kind angle .55 degrees and 20 degrees, TC-12 also can be used a powerful front fill system.

Each side panel has M8 threaded insert ,  used for quick and flexible install. The right part of the box gas ⌀35mm pole socket can be used for the installation of the sound box support. The bottom has rubber feet and provides antiskid function. The impedance of each loudspeaker for 8 ohms, and can be use 2 / 3 monitor for 1 group(4ohms / 2.7ohms)

Dimensions:Width: 447 mm (17.6 inches), height: 488 mm (19.2 inches), depth: 310 mm (12.2 inches), weight:33 kg (72.7 lbs.).

The cabinet shall be fitted with internal hardware and connected via two parallel NL-4 speakon.

www.qanon-audio.com

_____________________________________________________

Product Information Version-1.0

Application

The design and application of TC12 coaxial monitor system can be used in many functions. The monitoring angle is matched with two kinds angles, 55 degrees and 20 degrees, TC12 andV18 /S18 ultra low frequency loudspeaker ground stack integration. The addition support ⌀35mm pole socket can be used with S18, providing fast and simple ground and stack application.

Monitor Angle 55°（Fig 1）                   Monitor Angle 20°（Fig 2）

_____________________________________________________

Separate Area（Fig 3）                             Parallel Use（Fig 4）

_______________________________________________ ______

FOH（Fig 5）                                         Monitor+sub（Fig 6）

www.qanon-audio.com

_____________________________________________________

Product Information Version-1.0

TC12 Technical Specification

Type	                           Coaxial Enclosure

Frequency Response(Preset)	      60Hz-18kHz(±3dB)

Nominal directivity	               (-6dB)

Horizontal	                       90°

Vertical	                            60°

Monitor Angle	                   55°（1）

20°（2）

Drivers	                            HF：1×1.75"（Ferrite Magnet）

LF：1×12"（Ferrite Magnet）

Rated Power(AES / Peak)	       HF:：50W / 100W

LF:：300W / 600W

Maximum Peak SPL	               124dB/1m

Nominal Impedance	               HF:8Ω / LF:8Ω

Pin Connections	                   NL4=+1-1

Connections	                       2 x NL4 Speakon

Width	                           447mm

Height	                           488mm

Depth	                           310mm

Weight	                           16kg/35.2lb

Rigging and Handling

Handle	                          2 handles

Threaded	                      13x M8 threaded insert

Pole socket	                      1x35mm Pole socket

stand bar	                      4x 10mm*38mm(H*⌀)

Physical Data

Material	                          Baltic Birch Plywood

Finish	                          Dark grey/Black

Front	                          Polyester powder-coated steel grill

Rigging	                          steel

Accessories

Optional Accessories	            1x1 Cover

1x2 Touring case

www.qanon-audio.com

_____________________________________________________

Product Information Version-1.0

Dimensions

www.qanon-audio.com

TRANSPORTATION ACCESSORIES

TC12-Touring case: removable front case on wheels (two TC12)

AMPLIFIED CONTROLLER

1）C15 Power amplifier  4 x 1500W / 8ohms

2）Mon-Panel (4 inputs/Link ,4-ch SpeakON Audio Panel )

3) D44 4in4out processor

4) 8channel Power

5) 4U Rack

ASSOCIATED ENCLOSURES

TC15                                   TC12                       TC10

www.qanon-audio.com